## Slide 1: MINI GOLF ROBOT Project Report
Embedded Systems Lab
CS 308 Project
Vaibhav Gupta – 09005019
Arup Kumar Pal – 09005024
Neeraj Toshniwal – 09005039
Shrikant Nagori - 09005040

## Slide 2: Aim of the Project
To design a golf playing robot.
Given a hole (marked by a blue flag) and a red coloured foosball on a platform made of wooden ply covered with green velvet, our robot will try to hit the ball towards the hole as accurately as possible.
Robot operates under a set of constraints.
For example: size and weight of ball, distance of ball from bot etc.

## Slide 3: Working of the bot:
Look for a red coloured ball by rotating in a circle.
Keep on doing so until the ball is in centre of the frame.
Move towards the ball in a straight line and stop at a specified distance from the ball using the sharp sensor.
Align itself for rotating around the ball in search of the flag.
Bot stops after finding flag in the centre of the frame.
Calculate the angle of inclination from the flag height perceived.
Hit the ball.
Repeat from step I.

## Slide 4: Hardware requirements
Firebird V ATMEGA2560
  basic skeleton on which we will implement the golf-playing bot.
  IR sharp sensors already attached to Firebird.
Zig-bee (XBee 802.15.4 OEM RF module 2.4GHZ)
  used for communicating between the firebird and the PC
2 Servo motors:
  To rotate the camera
  To provide variable angle to the incline.

## Slide 5: Hardware requirements
Wireless camera
  used for taking snapshots
  TV tuner card is also used (for connecting to PC)
Platform
  made of plywood (4 ft X 4 ft) with a hole at one of the corners.
  covered with green velvet to provide friction to the ball.
Inclined Plane
  move ball by a variable distance
  consists of an aluminium angle that can be inclined at a variable angle to the horizontal plane by using servo motors

## Slide 6: Software requirements
AVR Studio 4 and WINAVR.
AVR Bootloader.
Matlab for Image Processing.
X-CTU for Zigbee configuration.

## Slide 7: Enumerating the Tasks:
1. Locate the Ball
2. Move towards the Ball
3. Rotate camera 90 degree to the right and bot 90 degree to the left .
4. Rotate in a circle around the ball trying to locate the flag.
5. Again revert back to original position i.e rotate camera 90 degree to the left and the bot 90 degrees to the right.

## Slide 8: Enumerating the Tasks:
6. Calculate angle of inclination from the height of the flag returned by image processing function.
7. Set servo angle accordingly.
8. Pick the ball and place it at the top of the incline for it to roll down freely.
9. Testing the model for various testcases.

## Slide 9: Enumerating the Tasks:
10. Image Processing for ball and flag.
11. Making a plywood platform and covering it with green velvet.
12.Setting up Zigbee connection between bot and PC.
13. Attaching inclined plane made from aluminium angle to a servo attached to the bot.
14. Fixing camera to a servo on top of the bot with proper inclination.

## Slide 10: Project Plan
Numerous new software and firebird functionalities in the project.
  planned to get a basic knowledge about all of them to test the feasibility of the project and divide up the work accordingly.
Divided the project into modules. (separate c code and image processing code)
We started with the easier tasks first.
Plan was to complete the project by 5th April and start on the documentation of the project
Following dates scheduled:
  Task 2-5 by 28th March
  Hardware along with Task 1 and 6 by 3rd April
  Remaining tasks by 5th

## Slide 11: Dates of completion
Task 2-5 by 1st of April( Done by Arup, Neeraj and Shrikant)
Hardware by 4th of April (Done by Vaibhav Gupta)
Task 1 and 6-8 by 9th of April( Done by Arup, Neeraj and Shrikant)
Remaining tasks by 10th April( Done by Arup, Neeraj, Vaibhav and Shrikant)

## Slide 12: Critical tasks
Calculate distance of the flag from the firebird.
Communicate through the Zigbee.
Hardware to hit the ball.(This can be improved drastically in extensions of the project.)
Achieve accuracy in hitting the ball.

## Slide 13: Innovation and Challenges
Innovations:
  Accurate hitting of the ball
    using Image Processing which was never tried before
  Algorithm is independent of the size of arena
    using flag for locating the hole helps achieve this
Challenges:
  The ball had a seam which caused the ball to deviate from the path towards the hole.
  The distance of the flag could not be calculated precisely and had to be converted into another notation for usage.

## Slide 14: Challenges
The firebird had issues with the motor and sharp sensor for which a lot of time was used up which was unnecessary.
Needed the bot to go straight ahead towards the ball, only when the ball is in the centre of frame.
Due to communication delay, bot rotated by an extra angle before stopping. To overcome this, we stopped one frame early.
This made the bot move directly towards the bot.

## Slide 15
Stage 1 Find the Ball
Stage 4
Hit the ball with appropriate force
Stage 3
Position itself to hit the ball
Stage 2 Move towards the ball
End
Ball fell into the hole
Stage 5
Check termination
FSM and its State Diagram:

## Slide 16: Tasks completed
Locate the Ball (1):
  used Image processing through Matlab for this task.
  ensured that the bot receives a signal to stop rotating and move towards the ball only when the ball is in the centre of the frame.
Move towards the Ball(2) :
  Simple motion of the firebird was used for this task.
  Used ADC Sharp sensor 11 to stop the firebird while at a safe distance from the ball to rotate around the ball.
  One could have also used ADC sensors 10 and 12 for more precision.

## Slide 17: Tasks completed
Rotate camera 90 degree to the right and bot 90 degree to the left(3) :
  keep the camera stable for image processing
  Adding the rotating feature to the camera could have made it unstable
  Used servo motors which locked the camera’s position. Wireless camera added to the stability.
  Used simple motion control of the firebird for rotating the bot.
  A wireless camera was mounted on a servo motor on top of the firebird . We used the servo motor to rotate the camera.

## Slide 18: Tasks completed
Rotate in a circle around the ball trying to locate the flag(4):
  Search for the blue flag while rotating around the ball.
  Used Matlab Image processing to accomplish this task.
  As soon as it locates the flag, the bot stops rotating around the flag.
  Major concern : orient the bot so as to able to hit the ball towards the goal.
  Ensured that the flag was a certain distance to the right of centre of the frame.
  This offset value depends on the width of the firebird and also the distance of the flag from the robot.
  Took only the width of the firebird into account.

## Slide 19: Tasks completed
Again revert back to original position i.e rotate camera 90 degree to the left and the bot 90 degrees to the right(5):
  The robot uses the servo motor to rotate back the camera to initial position ( 0 degree) and simple motion control to rotate bot by 90 degrees to face the ball and the flag.
Calculate angle of inclination from the height of the flag returned by image processing function(6):
  to hit the ball with variable force depending upon the distance of the flag from the robot.
  used Image Processing.
  The Matlab code returns values between 3- 9 which signifies distances of 10 cm to 90 cms.
  Major problem : signal processing in firebird can receive only one character at a time, this forced us to code distances into single digit values.
  Precision completely dependent on the ball used and the arena.
  efforts to make it universal.

## Slide 20: Tasks Completed
Set servo angle accordingly(7):
  The servo is initially at angle of 90 at which the incline is straight.
  Requires to set a lower value than 90 to hit the ball towards the flag.
  Kept a threshold angle of 45, so that the ball does not jump off after hitting the floor.
Pick the ball and place it at the top of the incline for it to roll down freely(8):
  One has to keep the ball at the very end of the incline

## Slide 21: Tasks Completed
Testing the model for various testcases(9):
  had a problem with the motion of the firebird as one of the motors was not working correctly
  Even replaced the motor, but the problem persisted
  Caliberation was done to values to achieve straight forward motion and rotating the bot in a circle.
  Various testcases mentioned later in the presentation were run

## Slide 22: Review Test Plan/Cases
Test Cases
  Ball not in the Arena : The firebird rotated 360 degrees and stops displaying Ball in Hole on L.C.D
  Ball and flag straight ahead of bot :
    Seeing the ball, the bot rotates towards the ball.
    It rotates 90 degrees and rotates camera also. It locates the flag immediately and re-aligns itself. The ball misses the hole by a small margin.
  Blue flag not in the arena : The bot after rotating around the ball for some time, stops and displays Flag not Found on L.C.D
  Ball was collinear to the flag and the bot. Distance between the ball and flag varied. The incline rose to a greater angle when the ball was near to the bot.

## Slide 23: Performance Metrics
Adjusted Communication delay for moving towards the ball
In case the delay changes, the bot will not be directly towards the ball
This would affect accuracy in a sense because we keep the flag at a certain distance from the centre in the frame. Also, the bot may hit the ball.
Needed to calculate the height of the flag.
For this , the camera needs to detect the entire flag and not some part of it.
If there was a difference in intensity of light, only some part of the flag was detected.
This resulted in the wrong angle of incline. So, we performed under a flash light to adjust for varying intensity

## Slide 24: Re-usability features
Any bot implementing the extensions of our project can use the entire code.
Functionalities can be appended at required places. functionalities.
The code is written mostly using functions and thereby is easy to work on. It also presents a working of the bot which is machine independent. The contents of the functions are to be changed on changing the underlying hardware.
The image processing code can be used for detecting any coloured object. Only a few parameters are to be changed to get desired output.

## Slide 25: Future Enhancements
One could improve upon our project and add for varying factors like sloped surface and obstacles between the ball and flag.
This would involve knowing the terrain and would make the simulation very much like actually playing golf.
One can build a golf stick arm attachment for the firebird or a grabber to place the ball into the incline
To achieve higher accuracy, one can involve the distance from the flag into calculating the offset.